## Slide 1
1st Workshop on Security and Dependability of Critical Embedded Real-Time Systems
ReSecure: A Restart-Based Security Protocol
for Tightly Actuated Hard Real-Time Systems
Fardin Abdi*, Monowar Hasan* Sibin Mohan, Disha Agarwal and Marco Caccamo
*These authors have made equal contribution to this work.

## Slide 2: Safety-critical CPS

## Slide 3
Our Idea:
Security Through
Frequent Restarts
And Fresh Reload

## Slide 4
Traditional Computers
Cyber-Physical Systems
Restarting
Past to Future
Notes: First, most of the bugs in production quality software are Heisenbugs \cite{candea2001recursive} which are hard to reproduce or depend on the timing of external events, for example race condition. Restarting is very effective in recovering from this type of bugs. Second, restarting can claim all the stale resources, clean up all the corrupt state (e.x. memory leaks, dangling pointers, damaged heap) and take system back into a known well-tested state within a predictable amount of time

## Slide 5: Why Restarts?
Reliably remove malicious components
Can be performed safely for real-time system
Can be initiated through HW WD timers

## Slide 6
Architecture
CC: Not verified, can create unsafe commands
SC: Can always keep the system safe
Decision Module: Predicts if the future states are safe
Watchdog timer: restart the board upon fail-stop
Rescue unit: bare-metal, verified
Main unit: OS/firmware can fail
RTOS
Decision Module
Safety Unit
Complex Unit
Complex Controller
WD Timers
RESET
PIN
Monitoring Unit
PeriodicTimers
Safety Controller
Sensors
- User Input
- Network Connection
- External Peripherals
- …
Read-Only Memory

## Slide 7
Physical Safety!
RTOS
Decision Module
Safety Unit
Complex Unit
Complex Controller
WD Timers
RESET
PIN
Monitoring Unit
PeriodicTimers
Safety Controller
Sensors
- User Input
- Network Connection
- External Peripherals
- …
Read-Only Memory
Complex unit may get compromised.
Physical plant remains safe.

## Slide 8: Adversary
Can Compromise Entire Complex Unit
Denial of Service Attacks
Information leakage through side-channels

## Slide 9: Triggering Restarts
Monitoring Unit
Hardware Watchdog Timers

## Slide 10: Monitoring Unit
Any technique can be implemented
However, still not 100% reliable

## Slide 11: Hardware Timers
Independent of Software will restart
Can recover the system when the monitoring unit is compromised
High Security
Lower Performance
Lower Security
Higher Performance
Restart Timer Period

## Slide 12: Optimal Periodic Restart Period

## Slide 13: Properties of Attacks

## Slide 14: Expected Unavailable Time

## Slide 15: Expected Damage

## Slide 16: Cost Function:

## Slide 17: Evaluation

## Slide 18: Evaluation
Complex Unit: Beagle bone black
Safety Controller: PC
Physical System: Hardware in the loop simulation of 3 degree of freedom helicopter

## Slide 19: Future Directions
Domain Specific Analysis of Attack
Randomization and Restarts

## Slide 20: Thanks!
Monowar Hassan
mhasan11@illinois.edu

## Slide 21: Support Slides

## Slide 22: Safety Controller Design
Goals:
To keep system within the Linear constraints
To satisfy the overrun constraints
To stay within the limits of actuators
Strategy:
To find a region where all the above are always satisfied
To design a state feedback controller that keeps the system within that region

## Slide 23: Switching Condition for Hard Constraints
Notes: \text{Reach}_{\leq T_{c}}(x, CC) \subseteq \mathcal{S}
\text{Reach}_{\leq T_s}(\text{Reach}_{\leq T_{c}}(x, CC), SC) \subseteq \mathcal{S}
\item$\text{Reach}_{= T_s }(\text{Reach}_{\leq T_{c}}(x, CC), SC) \subseteq \mathcal{R}